## Slide 1
U.S. EPA Region 9’s New Response Action Levels
02 October 2014
Derral Van Winkle, P.G.
NAVFAC Southwest, Environmental Restoration Program Manager

## Slide 2: Overview
Background
What are the EPA Region 9 response action levels?
Does State of California have guidance?
Comparison with other standards
Sampling considerations
What are the recommended potential response actions?

## Slide 3: Background
2011 – EPA Revised toxicity assessment for TCE in Integrated Risk Information System (IRIS)
December 2013 – EPA Region 9 issued a memorandum to SF RWQCB identifying some requirements for South Bay sites
  Similar to response levels issued in July 2014
  Terminology and concentrations changed slightly
July 2014 – EPA Region 9 issues memorandum with recommendations to division staff and management
  Identifies tiered response action levels which are based on acute, short term effects of TCE
  EPA cites National Contingency Plan and Superfund Guidance as basis for legal requirement for oversight on NPL sites
State of California DTSC – published HERO HHRA Note Number 5 on 21 August 2014
Notes: IRIS
Conclusion that EPA exposure poses non-cancer toxicity to developing fetus including fetal cardiac malformations
Women in first trimester are one of most sensitive populations to TCE inhalation exposure
Specifically 3 weeks in first trimester where heart is developing
  December 2013 – Prompt Response Action Level - > to Accelerated Response Action level
  Based on short term exposure not the typical long term chronic effects for evaluating risk
  NCP/Superfund give EPA authority to implement these actions on NPL investigations provide for early or interim actions where warranted by hazards posed by site-related contamination
  State Department of Toxic Substances Control (DTSC) Human and ecological risk office (HERO) published a Human Health Risk Assessment Note (No. 5) on August 21, 2014

## Slide 4: EPA Region 9 Response Action Levels
Tiered Concentrations
Exposure Scenario | Accelerated Response Action Level (HQ = 1) | Urgent Response Action Level (HQ = 3)
Residential | 2 mg/m3 | 6 mg/m3
Commercial/Industrial (8-hour workday) | 8 mg/m3 | 24 mg/m3
Commercial/Industrial (10-hour workday) | 7 mg/m3 | 21 mg/m3
Notes: Reference Concentration (RfC) is same as accelerated response action level for residential exposure because exposure is considered continuous (24 hour); includes a “margin of safety”
HQ = 3 is “generally Region 9 practice to immediately initiate response action to address exposures at or above an HQ=3”

## Slide 5: DTSC Response to EPA Region 9 Response Action Levels
Concurs with EPA residential and industrial setting response Levels
But:
  If in residential exposure scenario with TCE concentrations >1 mg/m3, or
  If in industrial exposure scenario with TCE concentrations >3 mg/m3
  HERO strongly recommends consulting the assigned HERO toxicologist assigned to the site to review TCE concentrations with respect to site-specific conditions

## Slide 6: OSHA/NIOSH TCE Standards Compared to 2014 EPA TCE Indoor Air Response Action Levels
6
Chart: Concentration (ug/m3)
09 July 14, EPA Region 9 Accelerated Response Threshold -Residential (ug/m3) | 2
09 July 14, EPA Region 9 Urgent Response Threshold - Residential (ug/m3) | 6
09 July 14, EPA Region 9 Accelerated Response Threshold - Industrial(ug/m3) | 8
09 July 14, EPA Region 9 Urgent Response Threshold - Industrial (ug/m3) | 24
NIOSH Relative Exposure Limit (ug/m3) - 10 Hour TWA | 134250
OSHA Permissible Exposure Limit (ug/m3) - 8 Hour TWA | 537000
~270,000 X less than OSHA PEL
~67,000 X less than OSHA PEL

## Slide 7: Sampling Considerations
Recommends sampling be time-integrated
  Accounts for temporal variability – average concentration over fixed time period
EPA advises quick turn around sampling if:
  Exposure of women of reproductive age exists
  Existing data indicate results that exceed response action levels
  Multiple lines of evidence suggest exceeding the response action levels is probable
  Confirmation samples if previous sampling indicated concentrations above the response action levels and early or mitigation actions were taken
DTSC guidance recommends seasonal sampling (e.g., warm and cool season)
  If first sample has concentration >0.48 mg/m3 and < response level – then obtain sample more quickly than seasonally
  Additionally, effectiveness of an interim action should be evaluated within a “few weeks”
  Concentrations > immediate response action should lead to actions within “a few days”

## Slide 8: Potential Response Actions
Tiered Responses
  Below Action Response Levels
    Recommend routine periodic sampling/monitoring
  Accelerated Response Action Level
    Early or interim mitigation and effectiveness confirmed promptly
    Sealing potential conduits (e.g., cracks, utility conduits)
    Increasing building pressurization or ventilation
    Treating indoor air
  Urgent Response Action Level
    Recommend mitigation measures initiated immediately and effectiveness confirmed before any additional exposure is allowed (temporary relocation may be indicated……)
Notes: Accelerated – within a few weeks
Urgent – HQ = 3

## Slide 9: Potential Response Actions
Tiered Responses
  Below Action Response Levels
    Recommend routine periodic sampling/monitoring
  Accelerated Response Action Level
    Early or interim mitigation and effectiveness confirmed promptly
    Sealing potential conduits (e.g., cracks, utility conduits)
    Increasing building pressurization or ventilation
    Treating indoor air
  Urgent Response Action Level
    Recommend mitigation measures initiated immediately and effectiveness confirmed before any additional exposure is allowed (temporary relocation may be indicated……)
  DTSC indicates success in immediately reducing indoor air concentrations with stand-alone air purifiers with carbon filter units and built-in air circulation fans
Notes: Accelerated – within a few weeks
Urgent – HQ = 3

## Slide 10: Summary
EPA Region 9 has issued tiered response action levels for TCE in indoor air based on updated toxicity information – NPL Sites
California state DTSC also has published guidance
Response action levels are orders of magnitude below legal short term exposure levels established by OSHA
Sampling should be time-integrated approach over defined time period
Response actions include wide variety of actions including revisions to building pressure/ventilation up to temporary relocation of building inhabitants
For concentrations > response action levels various interim actions and timeframes are recommended
  Sealing cracks to temporary relocation of occupants
  Few weeks to few days